## Slide 1
Kristoffer Carlsson
Division of Material and Computational Mechanics
Chalmers University of Technology
@KristofferC
kristoffer.carlsson@chalmers.se
An overview of the package
landscape for FEM in Julia
FEM in Julia
Notes: Kristoffer Carlsson
Material and computational mechanics division from Chalmers University of Technology,
Gothenburg, on the South West coast.
Tradition for new talkers at JuliaCon to say how they got started with Julia
For me, interactivity combined with performance, like to poke around in a REPL
Started writing some FEM code in pure Python, very slow, messing around with Cython and JIT annotations.
Tried Julia, blown away by performance and open source -> look under hood
TODO: generate images for RVE

## Slide 2
Macroscopic homogeneous response is a volume average of heterogenities on a smaller scale
Material models on macroscopic scale cannot predict new response to changes on the smaller scale
macro
meso
micro
Motivation

## Slide 3
Motivation

## Slide 4
Pre-processing
Assembly
Sparse Linear System
Post-processing
FEM Pipeline
Mesh generation
Tensor operations
Shape functions
Vizualization of solution
Aggregate data (plotting)
Geometry
Iterative solvers
Direct solvers
Plasticity, dense solver QP

## Slide 5
Full fledged Julia FEM package?
A full FEM stack is a huge project
  Deal.II – C++ - 30 000 commits – 20 years
  DOLFIN – C++ - 21 000 commits – 10 years
Julia public for 4 years
JuliaFEM.jl - @ahojukka5 et al.
EllipticFEM.jl - @gerhardtulzer
DifferentialEquations.jl -@ChrisRackauckas

## Slide 6
Pre-processing
Assembly
Sparse Linear System
Post-processing
FEM Pipeline
Mesh generation
Tensor operations
Shape functions
Vizualization of solution
Aggregate data (plotting)
Geometry
Iterative solvers
Direct solvers
Plasticity, dense solver QP

## Slide 7
Geometry + Meshing
Many existing free non-Julia tools for geometry + meshing. GMSH, netgen, tetgen etc.
Works well, however, need to read the generated mesh files into Julia
Meshio.jl - @SimonDanisch
  Currently, mostly computer graphics mesh formats
  I recently added ABAQUS .inp format (in a PR)
  Call to action!
Mesh readers

## Slide 8
Pre-processing
Assembly
Sparse Linear System
Post-processing
FEM Pipeline
Mesh generation
Tensor operations
Shape functions
Vizualization of solution
Aggregate data (plotting)
Geometry
Iterative solvers
Direct solvers
Plasticity, dense solver QP

## Slide 9
Tensor operations
Typically PDE’s are given as a collection of tensorial relations
Working with ”naked” Julia arrays as a representation of tensors possible
This is Julia! No fear of creating new types that maps more directly to our mathematical objects

## Slide 10
Einsum.jl - @ahwillia
TensorOperations.jl – @Jutho
Tensor operations
using Einsum
A = zeros(5,6,7)
X = randn(5,2)
Y = randn(6,2)
Z = randn(7,2)
@einsum A[i,j,k] = X[i,r]*Y[j,r]*Z[k,r]
using TensorOperations
α=randn()
A=randn(5,5,5,5,5,5)
B=randn(5,5,5)
C=randn(5,5,5)
D=zeros(5,5,5)
@tensor begin
D[a,b,c] = A[a,e,f,c,f,g]*B[g,b,e] + α*C[c,a,b]
E[a,b,c] := A[a,e,f,c,f,g]*B[g,b,e] + α*C[c,a,b]
end

## Slide 11
ContMechTensors.jl - @KristofferC
  Size of tensors known at compile time (1D, 2D, 3D), loop unrolling benefitial
  Symmetric tensors are common
  Stack allocation + infix notation  beautiful code
  Maps directly to assembly instructions, no SIMD yet.
Tensor operations
using ContMechTensors
A = rand(SymmetricTensor{2, 2})
B = rand(Tensor{4, 2})
x = rand(Vec{2})
A ⋅ x # dot product
A ⊗ A # open product
B ⊡ A # double contraction
det(A), inv(A), trace(A)
Notes: Typically Colon is used for double contraction, why didn’t I use it?

## Slide 12
Shape functions
After variational formulation
Discretization
Quadrature
Need to evaluate shape functions at quadrature points defined by
Notes: Typically Colon is used for double contraction, why didn’t I use it?

## Slide 13
Shape functions
JuAFEM.jl — @KristofferC, @fredrikekre
  Quadrature
  FastGaussQuadrature.jl for cubes, tables for tetrahedrons.
julia> quadrule = QuadratureRule(:legendre, Dim{2}, RefTetrahedron(), 1);
julia> points(quadrule)
1-element Array{ContMechTensors.Tensor{1,2,Float64,2},1}:
[0.333333,0.333333]
julia> weights(quadrule)
1-element Array{Float64,1}:
0.5
Notes: Typically Colon is used for double contraction, why didn’t I use it?

## Slide 14
Shape functions
julia> const dim = 2;
julia> basis_order = 1;
julia> basis = Lagrange{dim, RefTetrahedron, basis_order}();
JuAFEM.jl — @KristofferC, @fredrikekre
  Basis
Notes: Typically Colon is used for double contraction, why didn’t I use it?

## Slide 15
Shape functions
julia> fe_values = FEValues(quadrule, basis);
julia> ele_coords = [Vec{2}((0.0, 0.0)),
Vec{2}((1.0, 0.0)),
Vec{2}((1.0, 1.0))]
julia> reinit!(fe_values, ele_coords)
julia> q_point = 1;
julia> node = 2;
julia> shape_value(fe_values, q_point, node)
0.33333333333333
julia> shape_gradient(fe_values, q_point, node)
2-element ContMechTensors.Tensor{1,2,Float64,2}:
1.0
-1.0
JuAFEM.jl — @KristofferC, @fredrikekre
  FEValues = quadrature + basis
Notes: Typically Colon is used for double contraction, why didn’t I use it?

## Slide 16
BlockArrays
Coupled/mixed problem leads to block like structures
Desireable to have a Julia array type that represents this

## Slide 17
BlockArrays
BlockArrays.jl — @KristofferC, v0.5 only
Proposes an AbstractBlockArray interface, extension to AbstractArray
Two implementations of block arrays
  PseudoBlockArray — whole matrix stored contiguously
  BlockArray — each block stored contiguously

## Slide 18
BlockArrays
julia> A = PseudoBlockArray(rand(3,3), [2,1], [2,1])
2×2-blocked 3×3 BlockArrays.PseudoBlockArray{Float64,2,Array{Float64,2}}:
0.587037 0.443899 │ 0.801079
0.132292 0.196876 │ 0.972342
──────────────────┼─────────
0.800054 0.251887 │ 0.78099
julia> A[Block(1, 2)]
2×1 Array{Float64,2}:
0.801079
0.972342
julia> A[Block(1, 2)] = [0, 0];
julia> A
2×2-blocked 3×3 BlockArrays.PseudoBlockArray{Float64,2,Array{Float64,2}}:
0.587037 0.443899 │ 0.0
0.132292 0.196876 │ 0.0
──────────────────┼────────
0.800054 0.251887 │ 0.78099
julia> nblocks(A)
(2,2)
julia> blocksize(A, 1, 2)
(2,1)
julia> full(A); # returns the ”normal” matrix

## Slide 19
  LAPACK wrapped in Base Julia, ’nuff said?
  Plasticity  maximum dissipation principle  fulfill KKT condition in each quadrature point
  Need to solve small dense nonlinear system, number of unknowns
  100 000 elements, 4 quadrature points  400 000 systems to solve per Newton iteration
  Overhead in solver packages can dominate
  NLsolve.jl, Optim.jl + ForwardDiff.jl =
Dense solvers
function solve(f, x0)
# allocate temporary arrays
for i in iter
do_step(f, x)
end
return solution
end
function solve(f, x0, cache=SolveCache(x0))
# unpack cache (Parameters.jl, @mauro3)
for i in iter
do_step(f, x)
end
return solution
end
Notes: Julia of course has Lapack wrapped and it w
When do you need to solve dense systems in FEM?
One example is when you have plasticity, maximum dissipation principle -> KKT condition should be fulfilled in each quadrature point
Solve a nonlinear dense system in 10^1 variables
Many systems..
Overhead in solver packages.

## Slide 20
Pre-processing
Assembly
Sparse Linear System
Post-processing
FEM Pipeline
Mesh generation
Shape functions
Tensor operations
Vizualization of solution
Aggregate data (plotting)
Geometry
Iterative solvers
Direct solvers
Plasticity, dense solver QP

## Slide 21
Direct solvers
  Cholmod + UMFPACK — Comes with Julia, ”\”
  Pardiso.jl, Mumps.jl, Wrappers to C libraries
Iterative solvers
  IterativeSolvers.jl - @jiahao et al.
  KrylovMethods.jl - @lruthotto
  Krylov.jl - @dpo
  PyAMG.jl - @cortner — PyAMG wrapper with PyCall
  See Lars Ruthotto: Iterative Methods for Sparse Linear Systems in Julia: A Quick Overview
PETSc.jl — Jared Crean — Talk on Friday
Sparse Linear Solvers

## Slide 22
Pre-processing
Assembly
Sparse Linear System
Post-processing
FEM Pipeline
Mesh generation
Shape functions
Tensor operations
Vizualization of solution
Aggregate data (plotting)
Geometry
Iterative solvers
Direct solvers
Plasticity, dense solver QP

## Slide 23
Vizualization of solutions
Dominating format: .VTK + Paraview/Visit
WriteVTK.jl - @jipolanco
using WriteVTK
points = [0.0 0.5 2.0 1.0 2.0;
0.0 1.0 0.0 0.0 1.0;
0.0 0.0 0.0 0.0 0.0]
cells = [MeshCell(VTKCellType.VTK_TRIANGLE, [1, 4, 2]),
MeshCell(VTKCellType.VTK_QUAD, [2, 4, 3, 5])]
vtkfile = vtk_grid("my_vtk_file", points, cells)
vtk_point_data(vtkfile, rand(5), "point data")
vtk_cell_data(vtkfile, rand(2), "cell data")
vtk_save(vtkfile)
Notes: - If anyone has written an exporter for binary VTK you know it can be difficult, header has to be separately encoded

## Slide 24
Aggregate data (plotting)
Plotting landcape in Julia used to be quite fragmented
Thanks to @tbreloff and Plots.jl this is no longer the case
Dataframes.jl + JLD.jl + Plots.jl (PGFPlots.jl backend for publications)
using JLD
using Dataframes
using Plots
pgfplots()
df = load("data.jld")[”analysis_data"]
data = extract_data(df)
p = plot(data)
PGFPlots.save("pgfplot.tex", p.o, include_preamble=false)

## Slide 25
Kristoffer’s wishlist
Make working with stack allocated arrays easier
  Array – powerful but big and heap allocated
  Goto solution is tuples
  Generated code explosions, type inference problems, immutability not always desired
  See issue #11902
Facilitate not double paying lookup cost when mutating LinearSlow elements
  K[i,j] += 1.0  K[i,j] = K[i,j] + 1.0
  K sparse  [i,j] expensive, double paying
  See issue #15630 and
  https://github.com/KristofferC/UpdateIndex.jl

## Slide 26
Conclusions
  Package landscape for FEM is developed well enough to do actual work
  State of the art Automatic Differentiation makes local stiffness tangents a breeze to evaluate
  Possible to use Julia for only a part of the FEM stack by calling into Julia from C++ FEM libraries

## Slide 27
Swedish Research Council
Julia Computing
Thank you!
Acknowledgements
Slides
https://github.com/KristofferC/JuliaCon_FEM